## Slide 1
Community Meeting # 1 – April 11th, 2017
John Sighamony, VTA Project Manager
Adam Dankberg, Kimley-Horn and Associates
Eileen Goodwin, Apex Strategies

## Slide 2: Agenda
Presentation
  Project Background
  Existing Conditions
  Project Alternatives Examples
  Next Steps
Q&A
Input Activity

## Slide 3: Project Objectives
Enhance the safety, comfort, and reliability of sustainable transportation modes, while still accommodating drivers
Community-supported
Implementable

## Slide 4: Study Area

## Slide 5: Santa Clara

## Slide 6: Levi’s Stadium Events
Study considering pedestrian and bicycle circulation around stadium
Traffic circulation and parking not addressed by this study, but covered by Transportation Management Plan

## Slide 7: Study Process

## Slide 8: Existing Conditions

## Slide 9: Activity Levels
Average of 11,550 weekday light rail boardings and alightings at stations along corridor, plus thousands more passing through corridor
Over 18,000 daily autos in some segments
Several intersections with over 100 pedestrian crossings per hour
Four major regional bicycle/pedestrian trails cross the corridor

## Slide 10: Current Mode Split, Weekday 8-9 AM
Santa Clara
Tasman & Great America
(West Leg)
San Jose
Tasman & Cisco Way
(West Leg)
Based on 2015/2016 auto, bicycle, and pedestrian volumes and 2016 VTA LRT Ridership

## Slide 11: Light Rail Activity
Busiest Stations are:
  Tasman (1,914 daily boardings, including transfers)
  Great Mall (1,107 daily boardings)
  Old Ironsides (376 daily boardings)
  I-880 (369 daily boardings)
64 trips per day in each direction west of Tasman, 68 trips per day in each direction east of Tasman
New Mountain View – Alum Rock service will be starting later this year

## Slide 12: Traffic Volumes
Traffic volumes highest near I-880 and in Milpitas
Traffic heaviest eastbound in evening
Some congestion westbound in morning
Chart: Example Hourly Traffic Volume Distribution Tasman Drive, East of Great America Parkway (2016)
| 0 | 4.1666666666666664E-2 | 8.3333333333333329E-2 | 0.125 | 0.16666666666666666 | 0.20833333333333334 | 0.25 | 0.29166666666666669 | 0.33333333333333331 | 0.375 | 0.41666666666666669 | 0.45833333333333331 | 0.5 | 0.54166666666666663 | 0.58333333333333337 | 0.625 | 0.66666666666666663 | 0.70833333333333337 | 0.75 | 0.79166666666666663 | 0.83333333333333337 | 0.875 | 0.91666666666666663 | 0.95833333333333337
Westbound | 24 | 11 | 8 | 14 | 24 | 111 | 321 | 782 | 1287 | 1042 | 603 | 395 | 387 | 356 | 324 | 326 | 400 | 571 | 482 | 235 | 144 | 117 | 70 | 63
Eastbound | 26 | 9 | 8 | 4 | 13 | 27 | 70 | 156 | 328 | 341 | 256 | 326 | 408 | 453 | 520 | 863 | 1478 | 1848 | 1690 | 903 | 288 | 179 | 109 | 66

## Slide 13: Traffic Congestion During Peak Times
Great Mall Parkway, East of I-880
Tasman Drive, West of Cisco Way

## Slide 14: Excess Capacity During Off-Peak Times
Tasman & Morgridge
Tasman & Vista Montaña
Tasman & Old Ironsides

## Slide 15: Bicycle Facilities

## Slide 16: Bike Lane Improvement in Santa Clara
Extend recently completed buffered bicycle lanes to Lick Mill Blvd
Tasman & Vista Montaña

## Slide 17: Bicycle Facilities
Tasman & Zanker
Tasman & Lawrence

## Slide 18: Regional Trail Connections
Calabazas Creek Trail
San Tomas Aquino Creek Trail
Guadalupe River Trail
Coyote Creek Trail
Calabazas Creek Trail
San Tomas Aquino Creek Trail
Calabazas Creek Trail

## Slide 19: Pedestrian Facilities

## Slide 20: Sidewalk Facilities
Tasman & Tasman Ct
Tasman & Calle del Sol

## Slide 21: Pedestrian Crossings
Tasman & Birchwood
Tasman & N First

## Slide 22: Levi Stadium Access

## Slide 23: Transit Facilities

## Slide 24: Access to LRT Stations

## Slide 25: Collisions
Higher Frequency Collision Locations
Lawrence Expressway
Montague Expressway
Fair Oaks Avenue
Thompson Street
Great America Parkway
First Street
Zanker Drive
Higher Frequency Pedestrian/Bicycle Collision Locations
Alder Drive
Montague Expressway
Calle Del Sol
Lawrence Expressway
Rio Robles
S Main Street
Centre Point Drive

## Slide 26: Sunnyvale Missing Bicycle Lanes & Sidewalks

## Slide 27: Santa Clara Missing Sidewalks

## Slide 28: N 1st St & Tasman

## Slide 29: Tasman & I-880 Interchange

## Slide 30: Future Growth

## Slide 31: VTA’s BART Extension and Next Network

## Slide 32: Improvement Examples

## Slide 33: Bicycle Improvement Examples

## Slide 34: Pedestrian Improvement Examples

## Slide 35: Transit Improvement Examples

## Slide 36: Next Steps

## Slide 37: Study Process

## Slide 38: Online Survey
tasmansurvey.vta.org

## Slide 39: PROJECT INFORMATION
VTA Community Outreach
CALL US:
Phone: (408) 321-7575 TTY Only: (408) 321-2330
EMAIL US:
community.outreach@vta.org
VISIT US:
http://www.vta.org/tasmanstudy

## Slide 40: Input Activity

## Slide 41: Station One
Where do you live/What modes do you use on the corridor?
Place a dot on the map and on the board.

## Slide 42: Station Two
What do you use the corridor for?
Write how you use the corridor on the board.

## Slide 43: Station Three
Identify improvement priorities for the corridor.
Place a dot on the areas of highest priority.

## Slide 44: Station Four
Identify specific areas in need of improvement along the corridor.
Place a sticky note on the aerial map.

## Slide 45: PROJECT INFORMATION
VTA Community Outreach
CALL US:
Phone: (408) 321-7575 TTY Only: (408) 321-2330
EMAIL US:
community.outreach@vta.org
VISIT US:
http://www.vta.org/tasmanstudy